For lab 4 we implemented two CPUs to see if there was an improvement between using a single CPU and two CPUs to do a rotation transformation on an image.

The following results are the average number of cycles per frame that a single CPU preformed
the frame was rotating the image 350 degrees

One CPU : Average Cycles per CPU 185096693.9

Two CPUs: Average Cycles per CPU 121727169.5

from this we can see that using two CPUs uses 1.52 times less cycles per CPU which translates to about 1.52 times faster rendering time since both CPUs are running in parallel